ADS1806

User manual

Dear user,

Thank you for purchasing ADS1806 (Automotive Scan Tool 4 In 1 ). This manual (Android version) contains usage and after service, please read it carefully before using.

CONTENT

I.  Software Installation ................................................................................. 01

II.  Software Registration ............................................................................... 07

III. Software Upgrade ..................................................................................... 11

IV. Testing Instruction .................................................................................... 11

[ After Service ] ................................................................................................ 16

Note: ADS1806 is a 4 in 1 scan tool for OBD2, VW, TOYOTA & HYUNDAI.

I. Software Installation

1. Software download

Put software into mobile phone from CD or download software from internet.

1) Put  CD  into  CD-ROM  of  your  PC  or  Laptop,  open  it  and  copy  file  named “APK” into memory card of mobile phone;

2) Download software from website:

Steps 1: Open IE Explorer and visit: http://english.adsscan.com with your PC or Android Mobile phone (Figure-01).

Figure-01

Steps  2: Click the "Upgrade" interface and download the “APK” software into your PC or Android Mobile phone.

Figure-02

2. Program installation

Steps 1: Find a program named “Files Manager” in your mobile phone.

Figure-03

Steps  2:  Open the Files Manager >>> USB storage >>> Download >>> and  find out “ADS1806 Automotive Scan Tool 4 In 1.apk”;

Figure-04

Figure-05

Figure-06

Steps 3: click and it will display the interface as Figure-07, click the

“Install” button and start to install.

Figure-07

Figure-08

Steps 4: After complete installation, it will display "Application installed" :

Figure-09

Steps 5: Then the “ADS1806 Automotive Scan Tool 4 In 1” software icon will display on the application program interface (Figure-10).

Figure-10

II. Software Registration

Note: So far, ADS1806 Android version software needn’t register and just connect with Bluetooth to use.

Steps 1: Connect the Diagnostic Device to your mobile phone and ensure that the Bluetooth Diagnostic Device power indicator lights, then the green light flash.

Figure-11

Figure-12

Steps 2: Open mobile phone and enter Settings:

Figure-13

Steps 3: Open the Bluetooth and scan for the device:

Figure-14

Figure-15

Steps  4:  You  will  find ADS  device  and  click  it  to  pair  with ADS  device,  the Passwords is 1234 or may be 0000.

Figure-16

Figure-17

Steps 5: ADS device has been paired, then you can test directly.

Figure-18

# III. Software Upgrade

Open IE Explorer and visit: http://english.adsscan.com, click the "Upgrade" interface and download the latest  Android  version software to reinstall.

Figure-19

IV. Testing Instruction

Steps 1: Open your phone’s software main interface and enter “ADS1806 Automotive Scan Tool 4” software .

Figure-20

Steps 2: It will display interface of three titles as:

Figure-21

[ Scan ]: Car diagnostic testing into menu.

[ Manual ]: Equipment software installation and operation instructions.

[ Version ]: Wireless  Bluetooth  diagnostic  instrument  hardware  and  mobile phone testing software version information.

Steps 3: Choose SCAN and start to test as Figure :

Figure-22

Figure-23

Here’s OBDII/EOBDII Demo as follows:

Figure-24

Figure-25

Figure-26

.

Figure-27

Figure-28

Figure-29

Figure-30

Figure-31

Figure-32

|  | [ After Service ] ● Warranty: Within one year. ● URL: http://english.adsscan.com ● Tel/Fax: +86-755-89368397 ● E-mail: sales@adsscan.com |
| --- | --- |