SK176  Mercedes Benz EIS key Test Tool

新款奔驰BGA钥匙和NEC锁头很难识别好坏，给我们维修工作带来不便，我们开发出一个针对W204  W207  W212车型专用，可以识别锁头和钥匙好坏的测试仪。不用连接方向锁ELV，就能测试出锁头和钥匙的好坏

It was difficult to tell the new Mercedes-Benz BGA key and NEC EIS were working or not, and it caused much trouble for the repair work.  Now we have developed a Mercedes Benz EIS key Test tool specialized for W204, W207 and W212, the device can test whether the key and EIS is working or not without connecting with the direction lock ELV.

Operation Instruction:

1，按图连接好设备，通电12伏，LED2灯会亮 LED1亮1秒

钥匙插入LED1灯会一直闪烁，这时能听到蜂鸣器响1声，钥匙拨出来响1声LED1灯会停止闪烁，说明锁头和钥匙是正常的。(检测到ACC的时候蜂鸣器响1声，检测到合法钥匙LED1灯一直闪烁)

- Follow the next picture to connect the device, supply with 12V power adapter, LED2 indicator will flash and LED1 flash for 1 second

Insert the key LED1 will keep flashing with buzzer beep once, remove the key LED1 stops flashing and with buzzer beep once, which indicate the key and EIS are in good condition.

(Hear 1 beep when test ACC, LED1 indicator keep flashing when test legitimate key)

Tips:

2，如果钥匙插入时，LED2灯会亮，没有声音，拨出钥匙也没有响声，说明锁头是好的，钥匙不正常，也有可能是钥匙正常的锁头不正常。

- If LED2 indicator flashes with no beep when insert the key and no beep when remove the key, which indicates either key or EIS is not working.

3，新匹配的钥匙，刚插入锁头，钥匙灯亮，拨出钥匙，再插入钥匙灯亮即灭，这时能听到蜂鸣器响1声，拨出钥匙响1声，说明匹配的钥匙是成功的。有的要插拨5次才能识别到新的钥匙，请按自己的经验辨别好坏。

3. Insert the new programmed key into EIS, the LED indicator on the key flashes; remove the key and insert back into EIS the key indicator goes off immediately with 1 beep, remove  the key with 1 beep, which indicates the key has been successfully programmed.

Some locksmith may have to repeat insert-and-remove key for 5 times to identify the newly programmed key, it depends on locksmith’s experience.