ADS1800

User manual

Dear user,

Thank you for purchasing ADS1800(OBDII Scanner). This manual (PC version) contains usage and after service, please read it carefully before using.

CONTENT

I.  Member Registration ................................................................................ 01

II.  Software Installation ................................................................................. 03

III. Software Registration ............................................................................... 08

IV. Software Upgrade ..................................................................................... 14

V.  F.A.Q ......................................................................................................... 17

VI. After Service .............................................................................................. 23

I. Member Registration

Steps 1：Open IE Explorer and visit: http://english.adsscan.com

Figure-01

Steps 2: If you do not register, please register first. Click the "register" button

(Figure-02), then it will enter the registration interface (Figure-03).

Figure-02

Figure-03

Steps 4: Input info. all above and click “Register” button.

Figure-04

Steps 5: Now finish registration, pls login with “Username" and "Password" previously registered (Figure-05).

Figure-05

II. Software Installation

Note:

Before install the software, pls connect the USB cable between the PC and device and ensure the power indicator light light up.

Steps 1: Copy the content of CD to the desktop, then double click “set up”:

Figure-06

Figure-07

Steps 2: Click “Next” button again as Figure-08:

Figure-08

Steps 3: Click “Install” button as Figure-09:

Figure-09

Figure-10

Steps 4: It will required to install the USB driver as Figure-11:

Figure-11

Steps 5: Click “OK” button after USB driver installation as Figure-12:

Figure-12

Steps 6: Click “Finish” button as Figure-13:

Figure-13

Steps 7: Software installation successful, it will display two icons in the desktop:

Figure-14

Note:

- If your PC has installed the firewall or anti-virus software, it will prevent the diagnostic software running. Pls uninstall and try it again.

- If your PC doesn’t work with CD, pls go to our website and click the "Upgrade" interface to download the software.

Figure-15

III. Software Registration

Note:

If it is the first time you start OBDII Scanner Software diagnostic system, it needs to be registered, or can't scan. Before register user, pls connect the PC and USB cable with 12V power supply and available Internet.

Steps 1: Double click and start “ADS1800 OBDII Scanner” on the desktop as Figure-16:

Figure-16

Steps 2: Click “REGIST” button as Figure-17:

Figure-17

Steps 3: Click “OK” button as Figure-18, it will display interface as Figure-19:

Figure-18

Figure-19

Steps 4: Turn to website and sign in your registered account:

Figure-20

Figure-21

Figure-22

Steps 5: Enter “Get Registration Code” from background interface:

Figure-23

Steps 6: Put the Product Code and Rand Code into the forms and click “Register” button to get the Password.

Figure-24

Steps 7: Put the Password into the software and click “OK” button.

Figure-25

Steps 8: Click “OK” button as Figure-26:

Figure-26

Steps 9: Register successfully, it will automatically restart as Figure-27:

Figure-27

# IV. Software Upgrade

Steps 1: Double click ADS1500 Oil Reset Tool from the desktop as Figure-28:

Figure-28

Steps 2: Click “UPDATE” button as Figure-29:

Figure-29

Steps 3: Click “OK” button as Figure-30, and wait for check:

Figure-30

Figure-31

Steps 4: Put the Password and click “OK” button as Figure-32:

Figure-32

Steps 5: Click “CarUp” button and after finish, it will auto-logout and restart.

Figure-33

Note: If it is the latest version, it will notice as follows:

Figure-34

# V. F.A.Q.

1. If it displays as Figure-36 and still display after reoperate:

Figure-35

Possible problems:

1) Check the USB cable connection is reliable between the PC and device.

2) Check the USB driver software installation is correct.

3) Check the power indicator light of device if lit up.

2. If the USB driver install successfully, it will display in Computer Management as Figure-37:

Figure-36

3. Manually install USB driver:

# Steps 1: Right click “My Computer” and click “Properties” as Figure-38:

Figure-37

Steps 2: Click “Hardware” button as Figure-38:

Figure-38

Steps 3: Click “Device Manager” button and it will display as Figure-39:

Figure-39

Steps 4: Double click the blue dash area and select “Update Driver...”:

Figure-40

Steps 5: Click “Next” button as Figure-41:

Figure-41

Steps 6: Click “Next” button as Figure-42:

Figure-42

Steps 7: Then wait for wizard search as Figure-43:

Figure-43

Steps 8: If it display as Figure-44, pls click “Continue Anyway”:

Figure-44

Steps 9: Click “Finish” button and USB driver will display as Figure-45:

Figure-45

Figure-46

VI. After service

1. Guarantee period: One year warranty.

2. Web: http://english.adsscan.com

3. Phone/Fax: +86-755-89368397

4. E-mail: sales@adsscan.com