ADS1802

User manual

Dear user,

Thank you for purchasing ADS1802 (TOYOTA Scan Tool). This manual (Android version) contains usage and after service, please read it carefully before using.

CONTENT

I.  Software Installation ................................................................................. 01

II.  Software Registration ............................................................................... 07

III. Testing Instructions .................................................................................. 10

[ After Service ] ................................................................................................ 12

I. Software Installation

1. Software download

Put software into mobile phone from CD or download software from internet.

1)  Put  CD  into  CD-ROM  of  your  pc  or  laptop,  open  it  and  copy  file  named

“APK” into memory card of mobile phone;

2) Download software from website:

Steps 1: Open IE Explorer and visit: http://english.adsscan.com (Figure-01)

Figure-01

Steps  2:  Click  the  "Upgrade"  interface  and  download  the  software  on  your computer.

Figure-02

2. Program installation

Steps 1: Copy file“APK”into mobile phone memory card and find a program named “My Files”.

Figure-03

Steps  2:  Open  the  My  Files  >>> All  Files>>>  sdcard0>>> ADS1802 TOYOTA Scan Tool ,  and  find  out “ADS1802 TOYOTA Scan Tool.apk”;

Figure-04

Figure-05

Figure-06

Steps 3: click and it will display the interface as Figure-07, click the

“Install” button and start to install (Figure-9).

Figure-07

Figure-08

Steps 4: After complete installation, it will display "Application	installed" :

Figure-09

Steps 5: Then the “ADS1802 TOYOTA Scan Tool” software icon will display on the application program interface (Figure-10).

Figure-10

II. Software Registration

Steps 1: Connect the Diagnostic Device to your PC and ensure that the Bluetooth Diagnostic Device power indicator lights. And the green light flash.

Figure-11

Figure-12

Steps 2: Open mobile phone, enter Settings:

Figure-13

Steps 3: Open the Bluetooth and scan for the device:

Figure-14

Figure-15

Steps  4:  You  will  find ADS  device  and  click  it  to  pair  with ADS  device,  the Passwords is 1234 or may be 0000.

Figure-16

Figure-17

Steps 5: ADS device has been paired, then you can test directly.

Figure-18

III. Testing Instructions

Steps 1: Open your phone’s software main interface and enter “ADS1802 TOYOTA Scan Tool” software .

Figure-19

Steps 2: It will display interface of three titles as:

Figure-20

[ Scan ]: Car diagnostic testing into menu.

[ Manual ]: Equipment software installation and operation instructions.

[ Version ]: Wireless  Bluetooth  diagnostic  instrument  hardware  and  mobile phone testing software version information.

Steps 3: Choose SCAN and start to test as Figure :

Figure-21

|  | [ After Service ] ● Warranty: Within one year. ● URL: http://english.adsscan.com ● Tel/Fax: +86-755-89368397 ● E-mail: sales@adsscan.com |
| --- | --- |