Way of update EBOOT of DIII

As a way of update kernel of DIII was newly added(one key through the way of updating kernel by SD card),we made some modification to the programme of EBBOT.

If you press “8+OK”a tips “Press OK to make sure and continue update Firmware”appears ,it means that the EBOOT programme in your device is old version. You need to update EBOOT programme first and choose a convenient way to update DIII kernel.

After update EBOOT, it is necessary to update kernel.

Tips:Before update EBOOT,please instal D3 TOOL first.

Step 1:Press button number 8 and button OK at the same time, and turn the power on. When you see “Press OK to make sure and continue update Firmware”press OK, then it enter the procedure of updating.

Step 2:Connect D3 with a computer through Mini USB (purple color), you can see a tips "Found New Hardware wizard".As the image shown below.

D

Step 3: choose "install the software automatically", click "click"

Step 4:  If DIII tools have been installed already, choose the second“SEC SOC SMDK Board”in dialog box as shown below, and click "Next" to complete driving installation.

Step 5:Double-click Digimaster III PC Tools and choose "Kernel Update".

Step 6: Make sure the purple Mini USB is connected , then you can see " USB connect succeed"

Step 7: click "Kernel Update" and choose “EBOOT_20110427.bin” then click "OK" to start EBOOT programme update.

Step 8: After 10sec. the DIII screen appears a twinkling red 'YH' logo which means EBOOT update is complete.

After update EBOOT successfully,please turn the power off and choose a appropriate way to update the kernel.

TIPS: Please unload the anti-virus software and firewall temporarily in order to running the software normally.