Update Instructions for K518 Added Hibernation Function

Updated Device: Lonsdor K518

Updated Condition: for all K518 devices with working normally

Updated Content: Added Hibernation function; Kernel update supported

Updated Version: K518 APK V1.5.25

Preparation for Update:

- Power on the device or keep the battery level over 80%.

- Make sure wifi network is in good condition and the device receives signal normally;

Update steps:

- Click [One key update] and skip to below interface. Then click the first button to update system. When the update complete, click [OK] to reboot the device.

- After rebooting, click and enter [Settings] menu, you will find there are two additional function buttons: [Update Kernel ] and [Display Settings].

- Click [Update Kernel] first and skip to below interface, then press [Update] to update the kernel.

- Click [Install] after updating the kernel file. And the device will reboot to install kernel.

- Blank screen is normal during the installation. The whole process will take 5 minutes, be patient to wait and don’t restart the device manually.

- The update complete when the password input interface appears. Screen auto-lock in the [Display Settings ] is added.

- Enter [Settings]→[Display Settings] to adjust the screen brightness and screen auto-locking time .

- The benefits for update: Save power to prolong stand-by time. Auto standby function can prevent the device from being overheated in hot summer.